Remote Sensing
By Satish Waghmare
[Speaker Notes: Hi, my name is Satish and my topic is on Remote sensing using the Arduino.]

---
Project Goal:
Switch
Light
LCD
Bluetooth Connection
Temperature
Arduino
[Speaker Notes: The function of the device is to take periodic temperature and light readings. One of these readings are then displayed on the LCD screen. The user can switch between displaying light reading or temperature reading by pressing the switch. The device can also transmit these readings via Bluetooth, “but I must warn, this is still in debug mode”.]

---
The switch is connected to pin 2.
Pin 2 allows for use of interrupt in the Arduino.
[Speaker Notes: The Arduino has 2 interrupt, pins 2 & 3. This interrupts what ever code is running and allows for the specified function to run. In our case the function just changes the state of a variable which represents either LDR or TEMP.]

---
LDR: Light Dependent resistor
The LDR changes its resistance depending on the light
This is represented as an analog voltage.
We use Arduino analog pin A1 to read this voltage.
[Speaker Notes: The Arduino UNO has a build in 10-bit ADC. This converts voltage from analog-to-digital. We can represent this in a range from 0 to 1023. i.e 2^10]

---
Temperature sensor: TMP36
This like the LDR, TMP36 also outputs an analog voltage
This is convenient as we can also use the analog pins with this
We use the Arduino analog pin A0 to read this voltage.
[Speaker Notes: The TMP36 are low voltage, precision centigrade temperature sensors and provide typical accuracies of +_ 1 C at +_ 25 C and +_ 2C over the -40 C to +125 C temperature range. It is easy to connect, left pin goes to power (2.7-5.5 Volt), right pin goes ground and middle pin will have analog Voltage directly connected to temperature.]

---
LCD: Liquid crystal display
LCD displays Temperature and Light reading .
We use Arduino pin (13, 9, 5, 4, 3, 6)
LCD
[Speaker Notes: The LCD Library allow to control LCD display that are compatible with Hitachi HD44780 driver.]

---
Bluetooth Low Energy (BLE)
Like LCD, we display temperature and
light reading on Phone using BLE.
LCD
Bluetooth
[Speaker Notes: BLE Shield is design to work with Arduino boards and it allows to connect Arduino board with other BLE central device like smartphone, tablet.]

---
Component list
Bread Board
Push Button
Temperature Sensor
Light Dependent Resister
LCD Display
Bluetooth Low Energy (BLE) Shield